NEO-2 Quick Start Manual

1) VEMEC / NEMEC / V3FIT equilibria from Erika Strumberger and David Terranova:
e.g., /proj/plasma/Neo2/ASDEX-U/32138/

comment:
Erika‘s file format –> out_neo-2_XXX (Boozer file)
David‘s file format – wout_XXX.nc (VMEC) → Konvertierung in Boozer file notwendig

Ad David‘s VMEC / V3FIT equilibria:
/proj/plasma/Neo2/NTV/Boozer_files_perturbation_field/ASDEX_U/vmec2boozer/

./run_boozerpy.sh wout_XXX.nc NSURF

2) Converting Boozer files into the NEO-2 format:
i.e., decomposition with respect to toroidal mode number ‚n‘
e.g., /proj/plasma/Neo2/NTV/Boozer_files_perturbation_field/ASDEX_U/32138/

comment:
Copy / link Boozer file from 1) into the working directory.
Launch Matlab script extract_pert_field_asedex.m.
If necessary, adapt line 1-3 of the Matlab script (e.g., filename).

3) Plasma profiles for multi-species NEO-2 computations:
e.g.,
/proj/plasma/Neo2/NTV/ASDEX_INPUT_CONVERTER/30835_MULTISPEC_TEST/

a) Template for single-species computations:
impurity_profile_1spec.m

a) Template for multi-species computations:
impurity_profile.m

comment:
Profile data is provided by experimentalists in (usually) different formats.
Therefore a manual pre-processing of input data is nearly always necessary.
The necessary HDF5 input file for NEO-2 is generated in the Matlab script (line 458-EOF).
Look for „h5write()“ for necessary input.

4) Preparatory work for a NEO-2 run (example):
/temp/andfmar/NTV_220917_profileAUG32169woHelCore_vmecAUG32138_nspec2_ VphiProfFSAV/

a) Create „CODE“-directory:

git clone /proj/plasma/Git/NEO-2-MODULAR.git/ .

Change to „NEO-2-QL“-directory and create „Build“-directory.
Compile NEO-2 in „Build“-directory – cmake .. && make
Debug flags can be acitvated - cmake -DCMAKE_BUILD_TYPE=DEBUG . . && make

b) Create „RUN“-directory:

These input-files are required by NEO-2:
.) profile - multi_spec_aug32169_t4.1500.in
.) Boozer files – „aug_2_rmp-n0.bc“ (axisymmetric) + „aug_2_rmp-n1.bc“ (perturbation)
Please mind the length of the filename („aug-XXX.bc“) which has to specified within „neo.in“.
If Condor is used, a copy of the Boozer files should be stored in „/temp“.
.) Link executable neo_2.x from „Build“-directory into the „RUN“-directory
.) Copy neo.in into the „RUN“-directory und set switches properly:
For ASDEX-U follwing switches must be set -
„in_file=aug_2_rmp-n0.bc“, „lab_swi=10“ and „inp_swi=9“.
.) Copy neo.in into the „RUN“-directory und set switches properly:
For ASDEX-U follwing switches must be set

! settings for multi-species computations
&multi_spec
     lsw_multispecies = .true.
isw_multispecies_init = 1
fname_multispec_in='multi_spec_aug32169_t4.0210.in'
isw_coul_log = 0 ! 0: Coulomb logarithm species independent
isw_calc_Er = 1
isw_calc_MagDrift = 1
/

! settings for NTV computations
&ntv_input
        isw_ntv_mode = 0 ! unused at the moment
        isw_qflux_NA = 1 ! turn on(=1)/off(=0) computation of non-axisymmetric part
        in_file_pert = 'aug_2_rmp-n1.bc' ! 'tok-synch2-n3.bc' ! perturbation field file
        MtOvR = 0.0d0 ! toroidal Mach number (only important for Mach num scans)
        B_rho_L_loc = 0.0d0 ! Larmor radius times B
        isw_ripple_solver = 3 ! ripple_solver version
        isw_mag_shear = 1 ! turn on(=1)/off(=0) non-local computations (mag. shear)
/

5) Launch ./neo_2.x
NEO-2 runs in „profile“-mode und generates directories „es_XXX“

6) Change to directory „es_XXX“, generate hostfile „hosts“ and launch ./run_neo2.sh

7) Output „neo2_multispecies_out.h5“ is computed:
See /proj/plasma/Neo2/NTV/RIPPLE_SOLVER_NORMALIZATION/ for further documentation

8) Finally there exists a possibility to merge the HDF5 output files:
/temp/andfmar/NTV_220917_profileAUG32169woHelCore_vmecAUG32138_
nspec2_VphiProfFSAV/CODE/MULTI-SPEC-TOOLS/h5merge_multispec.f90

„final_neo2_multispecies_out.h5“ will be generated

Please mind that NEO-2 Output is given in cgs-units.

9) Plot NEO-2 output:
/proj/plasma/Neo2/NTV/AUG32169_DATA/NEO2_MULTISPEC_DATA_VMEC31021_
PROF32169/

see Matlab script „plot_4spec_ZWav_wHelCore.m“